## Slide 1: cumulus
CumulusLinux!
Draft: 22-Dec-2017
Open networking overview and command reference to ports, bridging, and static routing on hosts (ex: ubuntu) and network devices (cumulus)

## Slide 2
Open Networking – Poised to take off in data centers
Model built on merchant silicon that may provide fewer features than proprietary chips but enable a lower-cost and more flexible switching alternative
ODMs are the new vendors
Traditional network vendors like Cisco, Brocade etc. have outsourced much of their hardware like box and ASICs to ODMs like Quanta, Accton, Delta Neworks which are now selling white boxes directly with new brand names such as iwnetworks, edge-core networks, agema respectively
Networking vendors joining the arena
Vendors like Juniper Networks would make their software available on a less expensive bare metal switch with open-source hardware. The juniper OCX1100 can run software from any other vendor. Similar approaches can give advantage to the traditional vendors due to their tried-and-true networking software
Front Runners
Big Web Players like Facebook and Google have been building data-center networks out of generic hardware and homegrown software for years, which constitute 11 percent of all data-center switch ports
Cumulus Networks created the first Linux operating system for network hardware, they are also partnering with companies like Dell to offer its Linux network OS on Dell's networking hardware
Growing Eco System
According to Cliff Grossner, an analyst at IHS's Infonetics Research. By 2019, just over one-quarter of all data-center switch ports that are sold will be on open switches
Choice, lower OpEx / CapEx
Linux OS on bare-metal switches make automation easier and cheaper
The savings can be significant. The average selling price of 10-Gigabit and 40-Gigabit Ethernet ports was $308, while the price on bare-metal hardware was $112, according to Infonetics
Decouple software from hardware, program switches like Linux servers
Choice of OS - Open Network Install Environment ~ 4Mb mini-Linux installation
Open Source ~ Open Network Linux (ONL), Traditional Control Plane ~ Cumulus Linux, Pica8's PicOS, SDN Control Plane ~ Big Switch Network's Cloud Fabric
Terminology
ODM – Original design manufacturer; Bare metal switch – just the hardware, with no operating system, OS to be installed separately; White Box – Bare metal switch + Pre Loaded OS, mostly sold by ODMs with new brand names; Brite Box – Branded White Box, A traditional vendor tagging its brand name on an ODM Box; Note: Both White/Brite boxes likely to have the flexibility of installing a different OS

## Slide 3: Important notes
Help
man <command> #manual or <command> --help, ifquery --syntax-help
NCLU – Network command line utility
This is cumulus proprietary, and all the NCLU commands start with net
Deprecated commands / tools
The existing service command is being replaced on all distributions with the systemctl command.
ifconfig, arp, route but still available with net-tools package, inbuilt on cumulus Linux.
ifenslave #deprecated bonding tool
Similar Internetworking on hosts and network devices
One interesting thing to note with Linux, is that the tables, tools, and processes used by end-nodes to reach other end-nodes are exactly the same as those used by routers (layer 3 internetworking devices) to forward packets to end-nodes. The neighbor table is maintained dynamically based on the ARP protocol; however, it can be manually controlled with the ip neighbor command.
Kernel Modules
sudo modprobe 8021q #VLAN module/driver, not reqd. in cumulus
sudo modprobe bonding #Bonding module/driver, not reqd. in cumulus

## Slide 4: System info
uname {–a/m}
hostnamectl
hostname {–f}
hostname <hostname> #or ‘net add hostname <hostname>’, /etc/hostname, /etc/hosts, effective after re-login
ps {-ef} #view the running processes, -ef for long list format
systemctl status #view all the system services
sudo dpkg-reconfigure tzdata #time-zone, Asia/Kolkata for India

## Slide 5: Package management
apt / dpkg / rpm / yum – distrubution dependent
apt – for ubuntu and Debian
apt list –installed #to view the list of packages already installed
sudo apt update #doesn’t update any software, ensures we have the list of most recent versions of available packages from the update repository
sudo apt upgrade #to upgrade the OS
sudo apt install <package> --upgrade #to upgrade a packageip
sudo apt install <package> #to install a package
apt show <package> #to verify the package installation
Examples of packages:
iproute2 #ip <link/route/address>

## Slide 6: Important files and directories
/bin, /sbin, /usr/bin, /usr/sbin #executable programs, sbin has system tools
/dev #hardware devices
/etc #configuration files
/home #user home
/var #variable length files
‘/’ or ‘root’ is the highest point of the Linux file system. Everything including hardware is represented in Folder and File structure. In general, the baseline directory structure and usage of it should be the same across various Linux distributions as defined by the file system Hierarchy Standard (FHS). Viewing log files needs administrator (superuser / root) access.

## Slide 7: /etc
/etc/sudoers #the privileges for who can run what, edited by visudo
/etc/network/interfaces #CentOS or RHEL equivalent /etc/sysconfig/network-scripts, ifquery -a
/etc/network/interfaces.d/
/etc/dhcp/dhclient.conf
/etc/resolv.conf #local domains and server names
/etc/frr #free range routing
/etc/hostname
/etc/hosts #first point of lookup for any host prior to going out to the DNS server
/etc/nsswitch.conf #can include directory services like NIS+ or LDAP
/etc/cumulus/acl/*
/etc/cumulus/ports.conf
/etc/cumulus/switchd.conf

## Slide 8: /var
/var/log #log files
/var/log/syslog #system log
/var/lib/dhcp/*.leases

## Slide 9: File system - Interaction / Navigation
pwd #present working directory
ls #list out files and sub-directories, -l for long list
ls –la #list all details about each entry, -al can also be used
cd #change directory, try /, ~
rm #remove files
mkdir #make directory
rmdir #remove directory
cp #copy
nano #file editor, legacy ones – vi/emacs
echo $PATH #contents of the $PATH variable
./ #refers to the current working directory

## Slide 10: File system - Interaction / Navigation Contd.
which <command> #displays the path of the executable command
cat <file> #display file contents
less <file> #view one page at a time
grep <pattern> <file> #search for a pattern in a file flags –E, -i
head <file> #see the first few lines of a file
tail <file> #see the last few lines of a file, flag –f to view in real time
| #pipe or redirection

## Slide 11: File permissions
tuuugggooo
t – type #d: directory, -: file, l: link/shortcut, c: special file
u – user
g – group
o – others
Two most import types of objects in the Linux file system are directories(‘d’) and files(‘-’).

## Slide 12: User
sudo passwd root #to set the root password
vagrant@cumulus:~$ id
uid=1001(vagrant) gid=1001(vagrant) groups=1001(vagrant),27(sudo)
vagrant@cumulus:~$ whoami
vagrant
vagrant@cumulus:~$ sudo id #Root user – ID 0
uid=0(root) gid=0(root) groups=0(root)
vagrant@cumulus:~$ sudo whoami
root
Many systems prevent you from becoming the root user
with su and instead require you to use the sudo command

## Slide 13: Troubleshooting
ping <ip-address / url> #continuous ping
ping <ip-address / url> {-c<n>} #n no. of packets
traceroute <ip-address / url>
nslookup {ip-address / url}
netstat {-l} #active processes with active network interface connections, -l for listening services
ip –s link {show} {interface} #link statistics
sudo ifreload –a #after changes to the interfaces file

## Slide 14: Interface types
Loopback lo
Management eth0
Switch ports swp<a-b> #depending on the platform
sudo systemctl restart switchd.service #cumulus
other common interface names on Linux distributions are ens3*, enp0s3*. In a physical box, the switching service can be started after installing appropriate license

## Slide 15
Types of changes
Non-Persistent – lost after restart
ip <link/route/address> #iproute2 package, mostly installed by default
Examples:
sudo ifdown <interface> #or sudo ip link set <interface> <down>
sudo ip link set <interface> mtu <value ex:1500>
ip address add dhcp #or <ip-prefix> dev <interface>
sudo ip link add <bridge-name> type bridge {vlan_filtering} {id} #native vlan
sudo ip link set <interface> master <bridge-name>
sudo bridge vlan add dev <interface> vid <id> {pvid} {untagged}
ip route add default via <next-hop> dev <interface>
ip route add <ip-prefix> via <next-hop> dev <interface>
Persistent – retained after restart
NCLU (net add *) or Direct file modification - /etc/network/*
The forthcoming slides will focus on persistent changes

## Slide 16
description | NCLU | /etc/network/interfaces
Enable ports, all swps are admin down by default | net add interface <interface> | auto swp<x> iface swp<x>
Admin down ports | net add interface <interface> link <down> | auto swp<x> iface swp<x> {link-down yes} #if down
MTU | net add interface <interface> mtu 1500 | auto <interface> iface <interface> mtu 1500
IP Address – Dynamic / Static | net add interface <interface> ip address [dhcp #or <ip-prefix> gateway <next-hop>] | auto <interface> iface <interface> inet dhcp #or iface <interface> address <ip-prefix> gateway <next-hop>
Configuration - Ports

## Slide 17
description | NCLU | /etc/network/interfaces
Layer2 Bridge | net add bridge bridge ports swp<a-b>,<c>,<d-e> | auto bridge iface bridge bridge-ports swp<a> swp<b> bridge-vlan-aware yes
PVID | net add bridge bridge pvid <id> | auto bridge iface bridge pvid <id>
VLAN | net add vlan <a-c>,<j>,<x-z> | auto bridge iface bridge bridge-vids a b c j x y z bridge-vlan-aware yes
SVI | net add vlan <id> ip address <ip-prefix> net add vlan <id> ip address <second-ip-prefix> | auto vlan10 iface vlan10 address <ip-prefix> address <second-ip-prefix> vlan-id 10 vlan-raw-device bridge #to assoc. with the bridge
Configuration – Bridging / VLAN

## Slide 18
description | NCLU | Associated file and content
Default route | net add routing route 0.0.0.0/0 <interface/next-hop> | /etc/frr/frr.conf ip route 0.0.0.0/0 <interface/next-hop > #cumulus #or post-up ip route add default via <next-hop> dev <interface>
static route | net add routing route <ip-prefix> <interface/next-hop> | /etc/frr/frr.conf ip route <ip-prefix> <interface/next-hop> #cumulus #or /etc/network/interfaces post-up ip route add <ip-prefix> via <next-hop> dev <interface>
Configuration – Static routing

## Slide 19: Verify
ip link #mac
ip link show <interface>
ip address #mac and ip
ip address show {dev} <interface>
ip neighbor show #neighbor/ARP table, for communication in the same layer2 domain
ip route show #routing table
net show configuration files
net show interface <interface/all> #NCLU
net show bridge macs
net show bridge vlan
brctl show
bridge <link/vlan/fdb> show #links’ status, vlans traversing, and forwarding database management

## Slide 20: Bridge Mac == Mac of the firstly added interface

## Slide 21: Reference
https://cumulusnetworks.com
https://en.wikipedia.org/wiki/Filesystem_Hierarchy_Standard
https://www.freedesktop.org/wiki/Software/systemd/PredictableNetworkInterfaceNames/
http://www.smartpctricks.com/wp-content/uploads/2014/04/DHCPPackets-Establishment.png
Thank you
shakir@techie.com